## Slide 1: Computer Architecture BCT 2408
Desmond Oketch sct212-0083/2021

## Slide 2: Introduction
Computer technology has advanced dramatically over the past 60 years. Early computers were expensive and limited in power, but rapid improvements in technology and computer architecture have significantly increased performance.
The introduction of microprocessors in the late 1970s accelerated this growth, leading to a shift from large, custom-built machines to mass-produced, high-performance processors.
RISC (Reduced Instruction Set Computer) architectures emerged in the 1980s, focusing on instruction-level parallelism and cache optimizations, pushing computing performance to new heights.

## Slide 3: Cont…
By 2002, the steady increase in processor performance began to slow due to three major challenges: power limitations, reduced opportunities for instruction-level parallelism, and stagnant memory latency.
As a result, the industry shifted its focus from increasing single-processor speeds to adopting multi-core processors. Instead of relying solely on instruction-level parallelism, modern computing architectures emphasize thread-level and data-level parallelism, requiring programmers to write explicitly parallel code.
The shift to parallel computing represents a major evolution in computer design, focusing on efficiency and scalability to drive future performance improvements.

## Slide 4: Classes of computers
In the 1960s, computing was dominated by large mainframes used for business and scientific applications.
The 1970s introduced minicomputers, which enabled time-sharing, and supercomputers, which pioneered high-performance computing.
The 1980s saw the rise of desktop computers, replacing time-sharing and leading to the emergence of servers for large-scale computing services.
The 1990s brought the Internet, PDAs, and high-performance consumer electronics.
Since the 2000s, embedded computers have become dominant, powering everything from smartphones to appliances.
These shifts have redefined computing, leading to three main categories: desktops, servers, and embedded systems.

## Slide 5: Cont…
Desktops: Optimized for price-performance, with a focus on compute and graphics power. Newest microprocessors often appear first in desktops.
Servers: They prioritize dependability, scalability, and throughput. Downtime can lead to significant financial losses. Servers power the web, enterprise applications, and large-scale computing.
Embedded Systems: The fastest-growing category. Found in household appliances, mobile devices, and digital electronics. Performance is often real-time, with strict power and memory constraints.

## Slide 6: Defining Computer Architecture
Computer designers must balance performance, cost, power, and availability.
Architecture involves:
Instruction Set Design – Defines the programmer-visible instruction set (ISA).
Functional Organization – Determines how components interact.
Logic Design & Implementation – Includes circuits, packaging, and cooling.
ISA serves as the boundary between software and hardware.
MIPS and 80x86 are examples of modern ISAs.

## Slide 7: Components of Instruction Set Architecture (ISA)
Class of ISA – General-purpose register architectures (e.g., MIPS, 80x86).
Memory Addressing – Byte addressing; alignment affects performance.
Addressing Modes – Register, immediate, displacement (MIPS), and more in 80x86.
Operand Types & Sizes – Supports 8-bit to 64-bit integers and floating-point numbers.
Operations – Data transfer, arithmetic, logic, control flow, floating point.
Control Flow – Branches, jumps, procedure calls, and returns.
Encoding – Fixed-length (MIPS) vs. variable-length (80x86) instructions.

## Slide 8: Trends in Technology
To ensure long-term success, instruction set architectures must adapt to rapid technological changes. Successful architectures can last for decades—like the IBM mainframe, which has been in use for over 40 years.
Four key technologies shape computer evolution:
Integrated Circuit Logic Technology: Transistor count increases by 40–55% per year, but device speed improves more slowly.
Semiconductor DRAM: Capacity grows by 40% annually, doubling every two years.
Magnetic Disk Technology: Density increases have varied, but disks remain 50-100 times cheaper per bit than DRAM.
Network Technology: Advances in switching and transmission systems drive performance improvements.

## Slide 9: Performance Trends & Transistor Scaling
A major trend in computing is that bandwidth improves faster than latency. Over time:
Bandwidth has increased 100–1000×
Latency has only improved 10× This means designers must optimize for higher bandwidth rather than focusing only on reducing latency.
Transistor scaling has also driven progress:
Feature size shrank from 10 microns (1971) → 90 nanometers (2006)
Smaller transistors allowed microprocessors to evolve from 4-bit → 64-bit architectures
More transistors enabled advanced pipelining and caching

## Slide 10: Trends in Power in Integrated Circuits
Power Challenges in Scaling
Power must be distributed across chips using hundreds of pins and interconnect layers.
Heat dissipation is critical as power increases.
Dynamic Power Consumption in CMOS
Dominant factor: Switching transistors
Formula: P = ½ × C × V² × f
Reducing voltage significantly lowers power and energy.
Clock rate reduction saves power but not energy.
Example: Adjustable Voltage Impact
15% voltage reduction → 15% frequency reduction → Power decreases proportionally.

## Slide 11: Power Challenges and Mitigation Strategies
Increasing Power Consumption
More transistors and higher frequencies outpace reductions in capacitance and voltage.
Early microprocessors: tenths of a watt → Pentium 4 (3.2 GHz): 135W
Air cooling reaching limits → Chips integrate temperature diodes to adjust performance.
Mitigating Power Issues
Clock gating: Disables inactive modules to save energy (~60% power reduction).
Static power (leakage current) rising due to shrinking transistor sizes.
Solution: Voltage gating for inactive modules.
Multi-core processors: Lower voltage & frequency for efficient power management.

## Slide 12: Trends in Cost
Cost Reduction Factors
Learning Curve: Manufacturing improvements lower costs over time.
Volume Production: Higher production reduces cost per unit.
Commoditization: Competition in standardized products drives prices down.
Integrated Circuit (IC) Cost
Wafer Processing: Advanced technology increases costs, but efficiency helps.
Die Size Impact: Smaller chips have better yield, reducing overall costs.
Mask Costs: Designing new chips is expensive, impacting low-volume production.
Cost vs. Price
Competitive markets shrink profit margins.
Companies invest in research and development to balance cost and innovation.